## Slide 1: Subnetting
Not That Hard

## Slide 2: What is it?
A way to logically separate an IP network
Expressed in CIDR notation
ie. 192.168.1.76/24
Notes: CIDR: Classless Inter-Domain Routing
An ip address is 32 bits, 4 octets of 8 bits each
/24 in CIDR has 24 bits for network addressing and 8 bits for host addressing

## Slide 3: Calculate
192.168.1.167/28
28 bits for Network Addressing
28 % 8 = 4 bit
4 bits for Host Addressing
192.168.1.167/30
30 bits for Network and 2 bits for Hosts
Notes: Remember that binary is in reverse, so our 8 bits is ordered as 128 - 64 - 32 - 16 - 8 - 4 - 2 - 1
00100001 is 33, NOT 132

## Slide 4: How many Hosts and Subnets
192.168.1.167/28
Number of subnets available: (2 to the power of bits available) - 2
(2 to the power of 4) - 2 == 14 subnets
Number of hosts available: 2 to the power of bits available
2 to the power of 4 == 16
8 8 8 4/4
0000XXXX is a network address
1111XXXX is a broadcast address
Notes: Why -2 on subnets? all 0 subnet is a network address and all 1 is broadcast address

## Slide 5
192.168.1.167/28
8 8 8 4/4 - 4 bits for Subnet, 4 for hosts
Convert last octet to binary
10100111
Look at first 4 bits
Converted to base 10 for subnet mask - 160
Look at last 4 bits
Converted to base 10 for host address - 7